|  | Technical data sheet SAMAN TILE & GROUT CLEANER UGC |
| --- | --- |
| DESCRIPTION |
| Saman Tile & Grout Cleaner is a fast acting acidic cleaner formulated to remove common grout stains. It also removes efflorescence that occur on new ceramic joints and grout haze on ceramic tiles. It is a ready-to-use product. |
| PRODUCT SPECIFICATIONS |
| Appearance: clear liquid Odor: odorless pH: ~1 Density: 1.02 kg/l Solubility in water: 100% soluble VOC: 0 Storage: Store in a dry, cool and well ventilated place. Keep container tightly closed. KEEP OUT OF REACH OF CHILDREN. Shelf life: at least 1 year in a well closed container. |
| APPLICATION |
| Avoid skin and eye contact by wearing chemical-resistant gloves and protective lenses. Pre-test on an inconspicuous area. Do not use on marble or limestone. Grout Joints Sweep or vacuum all surfaces For best results, pre-wet the surface with water Apply the cleaner directly to the grout joints Let it works 15 seconds Scrub the surface with a soft brush or a scouring pad Rinse thoroughly with clean water Let it dry at least 2 hours before sealing it with Saman Grout Sealer Use the product on newly installed ceramic tiles to remove white stains caused by the grout. Ceramic Tiles Sweep or vacuum all surfaces Apply the cleaner with a scouring pad or a clean cloth Rub lightly Rinse thoroughly with clean water For a safe and correct use, read safety data sheet before handling the product. |

To the best of our knowledge, the information contained herein is accurate. Since conditions and methods are beyond our control, no warranty is expressed or implied as for the final result.  The user is advised to access the suitability of the product on a test area before application.